## Slide 1: IPSEC VPN ON SRX

## Slide 2: Network Diagram
172.168.3.3
Testing PC
SRX to SRX
192.168.3.3
Testing PC
172.168.3.254,3.3.3.3
SRX 1500
tunnel ipterface
3.3.2.6,3.3.2.5
3.3.3.4,192.168.3.254
SRX 340
IPsec | IKE Phase 1 | IPsec Phase 2
Encryption | Advanced Encryption Standard (AES); AES-256 | Advanced Encryption Standard (AES); AES-256
Authentication | Secured Hashing Algorithm (SHA); SHA2-256 | Secured Hashing Algorithm (SHA); SHA-256-128
Perfect Forward Secrecy (PFS) | DH - Group 20 86400 seconds | DH - Group 20 3600 seconds
IKE version | V1 | ---
Secret | Self-generated cert | ---

## Slide 3: Using RSA-signature SRX configuration
pki {
ca-profile 1500 {
ca-identity KK;
revocation-check {
disable;
}
}

## Slide 4: IKE config
ike {
proposal ike-proposal-1500 {
authentication-method rsa-signatures;
dh-group group20;
authentication-algorithm sha-256;
encryption-algorithm aes-256-cbc;
lifetime-seconds 86400;
}
policy ike-policy-1500 {
mode main;
proposals ike-proposal-1500;
certificate {
local-certificate 1500;
peer-certificate-type x509-signature;
}
}
gateway ike-gate-1500 {
ike-policy ike-policy-1500;
address 3.3.3.4;
external-interface ge-0/0/4;
version v1-only;
}
}

## Slide 5: IPSEC config
ipsec {
proposal ipsec-proposal-1500 {
protocol esp;
authentication-algorithm hmac-sha-256-128;
encryption-algorithm aes-256-cbc;
lifetime-seconds 3600;
}
policy ipsec-policy-1500 {
proposals ipsec-proposal-1500;
}
vpn ipsec-vpn-1500 {
bind-interface st0.0;
ike {
gateway ike-gate-1500;
ipsec-policy ipsec-policy-1500;
}
establish-tunnels immediately;
}
}

## Slide 6: IPSEC ON ROUTER
172.168.3.3
Testing PC
192.168.3.3
Testing PC
172.168.3.254,3.3.3.3
SRX 1500
tunnel ipterface
3.3.2.6,3.3.2.5
3.3.3.4,192.168.3.254
Cisco 2800
IPsec | IKE Phase 1 | IPsec Phase 2
Encryption | Advanced Encryption Standard (AES); AES-256 | Advanced Encryption Standard (AES); AES-256
Authentication | Secured Hashing Algorithm (SHA); SHA2-256 | Secured Hashing Algorithm (SHA); SHA-256-128
Perfect Forward Secrecy (PFS) | DH - Group 20 86400 seconds | DH - Group 20 3600 seconds
IKE version | V1 | ---
Secret | Self-generated cert | ---

## Slide 7: Using RSA-signature router configuration
crypto pki trustpoint 2900
enrollment terminal
subject-name CN=2900
revocation-check none
rsakeypair 2900
!

## Slide 8: IKE config
crypto isakmp policy 3
encr aes 256
hash sha256
group 20
!

## Slide 9: IPSEC config
crypto ipsec transform-set 33 esp-aes 256 esp-sha256-hmac
!
crypto ipsec profile 33
set transform-set 33
!
interface Tunnel1
ip address 3.3.2.5 255.255.255.248
ip nat outside
ip virtual-reassembly in
tunnel source 3.3.3.4
tunnel mode ipsec ipv4
tunnel destination 3.3.3.3
tunnel protection ipsec profile 33
!

## Slide 10: Nat setting
172.168.3.3
NAT:10.10.2.3
Testing PC
192.168.3.3
NAT:10.10.1.3
Testing PC
172.168.3.254,3.3.3.3
SRX 1500
Source NAT
3.3.3.4,192.168.3.254
Cisco 2800
IPsec | IKE Phase 1 | IPsec Phase 2
Encryption | Advanced Encryption Standard (AES); AES-256 | Advanced Encryption Standard (AES); AES-256
Authentication | Secured Hashing Algorithm (SHA); SHA2-256 | Secured Hashing Algorithm (SHA); SHA-256-128
Perfect Forward Secrecy (PFS) | DH - Group 20 86400 seconds | DH - Group 20 3600 seconds
IKE version | V1 | ---
Secret | Self-generated cert | ---

## Slide 11: NAT config
Router:ip nat inside source static 192.168.3.3 10.10.1.3
SRX:
source {
pool pool-1 {
address {
10.10.2.3/32;
}
}
rule-set srt {
from zone trust;
to zone vpn;
rule rou {
match {
source-address 0.0.0.0/0;
}
then {
source-nat {
pool {
pool-1;

## Slide 12: Checking command
SRX:show security ike security-associations
show security ipsec security-associations
show security flow session
Router:Show crypto iskamp sa
Show crypto ipsec sa

## Slide 13
Thank you !